## Slide 1
Relocation of Hardware Tasks across Networked Partially Reconfigurable FPGAs
E-CON UNI 2017 - Lima, November 24th, 2017
Aurelio Morales Villanueva, PhD
Universidad Nacional de Ingeniería

## Slide 2: Overview
Introduction and background
  Multitasking systems
  Field-Programmable Gate Array (FPGA)
On-Chip Context Save and Restore (CSR)
On-Chip Hardware Task Relocation (HTR)
Remote HTR across networked FPGAs
    Conclusions
    Future Work

## Slide 3: Task Switching Analogy
Multiple tasks execute concurrently
  Each task ≡ one bitstream
Multiple regions time multiplex tasks
  Use context save (CS) and context restore (CR) for task switching
  CS: saves flip-flops’ values
  CR: restores flip-flops’ values
Task relocation
  Tasks may run on different regions
  Challenging!
One task executes at a time
  Each task ≡ piece of binary code
  Time multiplex tasks
One stack for all tasks
  Stack saves context for task restore
No task relocation
No reconfiguration of μP
Hardware task N
Hardware task 2
Hardware task 1
μP or
custom HW
Region 3
Region 2
Region 1
FPGA
FPGA HW task switching
Software task N
Software task 2
Software task 1
Stack
OS
+
MMU
μP
Processor SW task switching
μP – Microprocessor
FPGA – Field Programmable Gate Array
OS – Operating System
MMU – Memory Management Unit

## Slide 4: What is an FPGA?
DSP – Digital Signal Processing Block
IOB – Input and Output Block
μP – Microprocessor
CLB – Configurable Logic Block
BRAM – Embedded RAM Block
FPGAs are programmable devices with large amount of resources connected with a complex, configurable routing network
  Logic resources: CLBs (LUTs, flip-flops)
  Special resources: BRAMs, DSPs, hardcore μP
  Routing resources: connection/switch boxes
Benefits of a FPGA over a traditional μP
  Application-specific hardware enables efficient processing at high frequency and low power
  Large logic fabric enables massive algorithm parallelism
  Flexibility: from combinational/sequential circuits up to system on chip (SoC)
  Allows time multiplexing of multiple designs (task switching)
Simplest hardware tasks: implemented in CLBs
  Occupy a portion of the FPGA = region
  Defined by a bitstream: size = depends on region size
  Task’s execution state (context) = flip-flops’ values
Xilinx CLB Architecture (partial)
Lookup Table (LUT)
flip-flop
IOB
IOB
IOB
BRAM
BRAM
BRAM
BRAM
BRAM
DSP
CLK
CLBs
CLBs
CLBs
CLBs
CLBs
CLBs
CLBs
Floorplanning of a Xilinx FPGA
region

## Slide 5: Reconfiguration on FPGAs
Benefits to system designers and functionality
  Run-time hardware adaptation via time multiplexing of resources
  Reduced area/power requirements
  Two types of reconfiguration: Full and partial reconfiguration
Full reconfiguration:
  Entire FPGA configured with full bitstream with fixed hardware task set
  Reconfiguration halts all tasks --- lengthy task switching time
  No context save/restore of hardware tasks --- tasks restart execution
Execution and state of all tasks are lost during full reconfiguration!
Configuration Port
Full bitstream 2
Full bitstream 1
HW task C1
HW task B1
HW task A1
HW task C2
HW task B2
HW task A2

## Slide 6: Partial Reconfiguration (PR)
  Increased flexibility
  Increased task throughput/performance
  Enhances hardware multitasking
    Requires context save and context restore for effective task switching
PR plays a key role in our research
PR compared to full reconfiguration
  Dynamic, on-the-fly reconfiguration of individual PRRs
    No interruption of static region or other PRRs!
  Uses partial bitstreams --- smaller than full bitstreams
    Faster reconfiguration time
    *May* require a bitstream for each PRM-to-PRR mapping
PR divides the FPGA fabric into two regions
  Static region: fixed functionality, never reconfigured after initial configuration at startup
  Reconfigurable region: multiple PR regions (PRRs)
    PRRs execute PR modules (PRMs) (hardware tasks)
Function
Power On
Time
Static region operation
Reconfiguration
Overhead
Configuration
Overhead
Module D
Module C
Module B
Module A
Embedded
processor
ICAP
Mem Controller
Reconfig. region
Static region

## Slide 7: On-Chip Context Save and Restore

## Slide 8: On-chip Context Save and Restore (CSR)
LSR – Local Set/Reset
GSR – Global Set/Reset
Purpose
  Save and restore the task execution state (flip-flops’ values)
CSR in Xilinx FPGAs
  Comprises two steps: context save and context restore
Context Save (CS)
  Capture and save the flip-flops’ values in off-chip file
Context Restore (CR)
  Restore previously captured flip-flops’ values
S/R CTRL – Set/Reset Control Logic
M2 – Configuration Memory bit

## Slide 9: On-chip CSR Operation
Reconfigure
PRR4
Execute
Execute
now
M5
PRR3
Context
Save
Context
Save
Resume
Execution
Context
Restore
M7
PRR4
M8
PRR4
M6
PRR3
M4
PRR2
M3
PRR2
M1
PRR1
M2
PRR1

## Slide 10: On-Chip Hardware Task Relocation

## Slide 11: On-chip Hardware Task Relocation (HTR)
On-chip CSR enables hardware multitasking on the same PRR
  May not maximize PRR utilization
    PRRs may be busy (tasks cannot be preempted)
    PRRs may be idle (pending tasks cannot execute on other PRRs)
Solution: on-chip HTR
  Extend on-chip CSR functionality
    Allow context restore (CR) on idle/different PRRs
    Maximize PRR utilization (more candidate PRRs for task execution)
HTR requires more complex bitstream manipulations than CSR
  Different PRR sizes and row and/or column locations
  PRRs with heterogeneous resources
  PRRs with different resource organization

## Slide 12: On-Chip HTR Operation
Example system
Execute PRM2 on PRR2
Context restore of PRM2 on PRR2
TCR2
Saved context relocation of PRM2 in PRR2
Trelocate
Context save of PRM3
TCS2
Hardware task relocation (HTR) of PRM2 on PRR2
Execute PRM2 on PRR1
Context restore of
PRM2 on PRR1
TCR1
Merge saved context of PRM2 with initial bitstream of PRM2
Tmerge
Context save of PRM1
TCS1
Context save and restore (CSR)
N
Y
PRR1 free or priority PRM
Execute PRM2
N
Y
Enable FPGA protection
Reconfiguration of PRR1 with PRM1
Tprotect_FPGA
Treconfig_PRR
Initialization
PRR2
PRR1
PRM3
Merged PRM2
PRM2
PRM
2
PRM
1
PRM2 executed in PRR1
and saved the context
Executing PMR3
Initial conditions

## Slide 13: Remote HTR (rHTR) across Networked Partially Reconfigurable FPGAs

## Slide 14: Remote HTR (rHTR) across Networked PR FPGAs
rHTR implements a distributed context relocation of PRMs in a network of PR-capable FPGAs
  Each FPGA in the network = node
  Transfer PRMs’ context via node switching
rHTR leverages CSR and HTR
  Prevent losing execution state of PRMs during node switching
  Maximize PRR utilization among all nodes in the network
Example systems
  Dynamic load balancing of hardware tasks, sensor networks, continuous adaptive target tracking, distributed fault tolerant systems, distributed/parallel processing of hardware tasks
Example: load balancing in a network of FPGAs
PRR4
PRR1
PRR2
PRR3
PRR4
PRR1
PRR2
PRR3
FPGA Node 1
FPGA Node 2
Example: Continuous adaptive target tracking
PRR4
PRR1
PRR2
PRR3
M1
PRR1
M2
PRR2
Slow Tracking
M3
PRR2
Fast Tracking
M4
PRR3
M4
PRR1
PRR4
PRR1
PRR2
PRR3
M1
PRR1
M2
PRR2
M3
PRR3
M4
PRR4
DDRM
DDRM
DDRM
M3
PRR1
M4
PRR2

## Slide 15: Motivations and Challenges
Motivations
  Maximize resource utilization in a network of PR-FPGAs
    Leverage CSR and HTR across nodes
  Maximize task throughput
    Improve task scheduling in a network of PR-FPGAs
    Task relocation between nodes
  No previous work in this direction!
Challenges
  Preserve task’s execution state on node switching
  Maintain node status consistency across all nodes
  Remote execution of PRMs across nodes
  Node switching latency

## Slide 16: Node Consistency in rHTR
Due to rHTR’s distributed nature, inconsistencies in the network of FPGAs must be avoided
  Global Table (GT) and Local Table (LT) on each node
  GT: Local and remote PRM-to-PRR mappings on all nodes
  LT: Node´s current PRM-to-PRR mappings
  Remote Procedure Call (RPC)
  Programs in a local node remotely execute code in a remote node
  Propagate/check PRMs/PRRs’ status across nodes
wired or
wireless
network
M7
PRR3
M6
PRR2
M5
PRR1
node 1
M3
PRR3
M2
PRR2
M1
PRR1
node 0
No broadcast of M8’s new status
No broadcast of M4’s new status
context restore
M8
M10
PRR1
M8
PRR4
M9
PRR1
M9’
PRR4
M4
PRR4
X
X
remote
relocation
M9 mapped in
node 1, PRR4
resume
execution
M8 abruptly ends
execution w/o
saving the context
schedule
later
M10 mapped in
node 0, PRR4
start
execution
context
save M4
X

## Slide 17: On-chip rHTR Operation
Preempted
Executing
PRM
status
S2
S1
priority
execution
levels
Critical
High
Medium
Low
P4
P3
P2
P1
MXY
PRR Z
Module Y
Node X
PRR Z
PRR
busy
PRR
free
PRR
unlocked
PRR
locked
wired or
wireless
network
node 3
PRR1
PRR2
PRR3 PRR4
P2
P2
P3
P1
M34
PRR4
M33
PRR3
M32
PRR2
M31
PRR1
remote
relocation
resume
M35
node 2
PRR1
PRR2
PRR3 PRR4
P2
P3
P3
P4
P1
M25
PRR2
M25
PRR1
M24
PRR4
M23
PRR3
M22
PRR2
M21
PRR1
resume
M25
context
save M22
local
relocation
X
node 1
PRR1
PRR2
PRR3 PRR4
context restore M15
context
save M12
P4
P4
P3
P2
P1
M15
PRR2
M14
PRR4
M14
PRR1
M13
PRR3
M12
PRR2
M11
PRR1
resume
M15
start
execution
X
node 0
PRR1
PRR2
PRR3 PRR4
context
save M04
P4
P3
P2
P1
M04
PRR4
M03
PRR3
M02
PRR2
M01
PRR1
preempt M04
start
execution
M35
PRR1
X
X
M05
PRR4
P4
S2
S2
S2
S2
S2
S2
S1
S1
S1
S2
S2
S2
S1
S1
S1
S2
S2
S2
S1
S1
S1
S2
S2
S2

## Slide 18: rHTR Flow: remote relocation of PRM
Start/resume execution of PRM in remote busy candidate PRR
  Lower remote priority PRM is preempted
Start/resume execution of PRM in remote free candidate PRR
Remote PRR is unlocked
Purple box contains the remote HTR (rHTR) steps

## Slide 19: Experimental results
Purpose
  Evaluate how PRR resources/size affects rHTR execution times
  Help system designers trade off PRR sizes, partial bitstream sizes, and rHTR times
Experimental setup
  Four Xilinx Virtex-5 ML509 board (four FPGA nodes) running Linux
  Gigabit Ethernet switch to interconnect the boards
  Two reconfigurable regions (PRRs) per FPGA node
    Three hardware tasks (PRMs) share the same PRR
    Each PRM: CLBs (flip-flops and LUTRAM) and BRAM resources
    Heterogeneous PRR sizes and FPGA fabric locations
  Global and local tables on each FPGA node
    Local and remote PRM-to-PRR mapping
  Task relocation cases (local or remote)
    Small-to-large PRR task relocation
Notes: For the purpose of HTR, two PRRs have different locations in the FPGA fabric.
There are two cases for relocation: from small-to-large PRR or from large-to-small PRR
The third case is not interesting: same-size PRR relocation
Since there are so many combination (144 for consecutive CLB columns) to perform a task relocation (in terms of sizes between two PRRs), I reduced the experiments (went down to 12) by having the large PRR with double (2x) the number of columns of the small PRR.
Since we covered only CLBs, doubling the number of columns in the large PRR, also doubles the number of frames.

## Slide 20: On-Chip rHTR results (1)
Texe1 shows non-linear growth rate
  Trhtr shows non-linear behavior as small-to-large PRR task relocation in HTR
Tftp_bit = 412 ms
  Independent of CS bitstream size (22 KB to 29 KB) in experiments
Remote destination PRR has twice as many CLB columns as compared to source local PRR
Start/resume execution of a PRM on a free and unlocked remote PRR (Texe1)

## Slide 21: On-Chip rHTR results (2)
Texe2 shows non-linear growth rate
  Tcs_rtask depends on the LUTRAMS, BRAMs, and flip-flops of remote task
  Trhtr shows non-linear behavior as small-to-large PRR task relocation in HTR
Tftp_bit = 412 ms as in Texe1
Remote destination PRR has twice as many CLB columns as compared to source local PRR
Start/resume execution of a PRM on a busy and unlocked remote PRR executing a lower priority PRM (Texe2)
Notes: CS bitstreams for the preempted tasks range from 22 KB to 28.9 KB. Partial bitstreams range from 31.9 KB to 95.4 KB

## Slide 22: Wrap-Up

## Slide 23: Conclusions (1)
On-chip context save and restore (CSR) software effectively implements hardware multitasking over the same PRR
  Autonomous, no design/system constraints
Extend on-chip CSR to implement on-chip hardware task relocation (HTR) software
  Task relocation between 2-D heterogeneous PRRs
  Maximize shared resource utilization on a single FPGA
Leverage CSR and HTR to implement on-chip remote HTR (rHTR) across networked PR FPGAs
  Maximize PRR utilization in a network of PR-capable FPGAs
    More candidate PRRs per hardware tasks

## Slide 24: Conclusions (2)
CSR, HTR, and rHTR for newer FPGA architectures
  CSR, HTR, and rHTR are valid for newer architectures
  Portable across different FPGA architectures
rHTR application domains
  Dynamic load balancing of hardware tasks across FPGAs
  Distributed fault-tolerant systems
  Distributed/parallel processing of HW tasks in a network of FPGAs
Experimental results on CSR, HTR, and rHTR
  Most attractive for smaller PRRs
  Enable system designers to determine application partitioning
    Number of hardware tasks (PRMs)
    PRM-to-PRR mappings (local or remote)

## Slide 25: Future Work
Optimize CSR, HTR, and rHTR execution times
  Use custom hardware to accelerate execution times
    Replace/combine software with custom hardware
rHTR for a mixture of different FPGA architectures
  Work with Zynq 7000 devices
    Zedboard, Parallella boards
On line software (or hardware) scheduler for rHTR
  Use configuration prefetching and reuse techniques
  Hardware/software (HW/SW) migration
  Execute/resume SW (or HW) task as a HW (or SW) task

## Slide 26: Publications
Published (4 conference)
  Morales-Villanueva, A., and Gordon-Ross, A., “On-Chip Context Save and Restore of Hardware Tasks on Partially Reconfigurable FPGAs”, 21st IEEE International Symposium on Field-Programmable Custom Computing Machines (FCCM’13), pp. 61-64.
  Morales-Villanueva, A., and Gordon-Ross, A., “HTR: On-Chip Hardware Task Relocation for Partially Reconfigurable FPGAs”, 9th International Symposium on Applied Reconfigurable Computing (ARC’13), LNCS vol. 7806, 2013, pp. 185-196.
  Morales-Villanueva, A., and Gordon-Ross, A., “Partial Region and Bitstream Cost Models for Hardware Multitasking on Partially Reconfigurable FPGAs”, 2015 IEEE International Parallel and Distributed Processing Symposium Workshop (IPDPSW’15), pp. 90-96.
  Morales-Villanueva, A., Kumar, R., and Gordon-Ross, A., “Configuration Prefetching and Reuse for Preemptive Hardware Multitasking on Partially Reconfigurable FPGAs”, 2016 Design, Automation and Test in Europe Conference & Exhibition (DATE), pp. 1505-1508.

## Slide 27: Questions?

## Slide 29: Additional Slides

## Slide 30: DDRM Flow: remote HTR (rHTR)
Resume execution of PRM in remote free candidate PRR
  Merge CS bitstream of scheduled PRM with initial partial bitstream of PRM in remote candidate PRR
  Execute CR by downloading the merged bitstream in the remote candidate PRR
Start execution of PRM for the first time in remote free candidate PRR
  Download initial partial bitstream of scheduled PRM in remote candidate PRR