## Slide 1
Partial Region and Bitstream Cost Models for Hardware Multitasking on Partially Reconfigurable FPGAs
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
Aurelio Morales-Villanueva and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA
This work was supported by National Science Foundation (NSF) grants EEC-0642422 and IIP-1161022, and Programa de Ciencia y Tecnología (FINCyT) under contract 121-2009-FINCyT-BDE

## Slide 2: Introduction
Field-programmable gate arrays (FPGAs)
  Programmable devices with large amount of resources
    Resources connected with a complex, configurable routing network
  Logic resources: CLBs (LUTs, flip-flops)
  Special resources: BRAMs, DSPs, hardcore μP
Reconfiguration on FPGAs
  Benefits system designers and functionality
    Run-time hardware adaptation via resource time multiplexing
    Reduced area/power requirements
    Two types of reconfiguration: full and partial reconfiguration

## Slide 3: Full Reconfiguration
Used for initializing the entire FPGA
  Entire FPGA configured with full bitstream and fixed hardware task set
  Reconfiguration halts all tasks (i.e., the entire system)
  Lengthy switching time if task set changes
Execution and state of all tasks is lost during full reconfiguration!
Configuration Port
Full bitstream 2
Full bitstream 1
HW task C1
HW task B1
HW task A1
HW task C2
HW task B2
HW task A2

## Slide 4: Partial Reconfiguration (PR)
Current FPGAs support PR
  Enables efficient hardware multitasking
  FPGA area and power reduction, faster configuration, etc.
Effectively leveraging PR on FPGAs
  Challenging for system designers
  Early design decisions affect overall PR system performance
  Inappropriate decisions severely degrade PR system performance
    Potentially worse than non-PR system
PR divides the FPGA fabric into two regions
  Static region: fixed functionality, never reconfigured after initial configuration at startup
  Reconfigurable region: multiple PR regions (PRRs)
    PRRs execute PR modules (PRMs) (hardware tasks)
Module D
Module C
Module B
Module A
Embedded
processor
ICAP
Mem Controller
Reconfig. region
Static region

## Slide 5: Partial vs. Full Reconfiguration
Increased flexibility
Increased task throughput/performance
Reduced FPGA area requirements
Reduced power consumption
Dynamic, on-the-fly PR of individual PRRs
  No execution interruption of static region or other PRRs!
Uses partial bitstreams
  Smaller than full bitstream  faster reconfiguration time
  *May* require bitstream for each PRM-to-PRR mapping
Function
Power On
Time
Static region operation
Reconfiguration
Overhead
Configuration
Overhead

## Slide 6: System Designer Challenges
  Fine-grained to coarse-grained partitioning
    Simple operations to entire application as a single PRM
  Designers can only evaluate a subset of these designs
    Need analytical or simulated cost models
    Evaluate design decisions’ impact on PRR size/organization and partial bitstream sizes
    Cost models avoid lengthy PR design flow
PR partitioning design space is exponentially large
Critical design decisions done in early system design
Static
region
Resource utilization vs. PRR size/organization
OR
PRR
1
PRR 1
PRR 2
PRR 2
PRR 2
PRR 1
PRR 1
PRR 1
PRM3
PRM4
PRM2
PRM1
PRR size/organization?
PRR size? How big?
PRM-to-PRR mapping?
Design partitioning?

## Slide 7: Motivations
Prior works in PR cost models
  Only provided partial methods for evaluating design tradeoffs
Manual PRR floorplanning process in the PR design flow
  Avoid oversized PRRs
  Avoid ill-suited PRR organizations
  Goal: high resource utilization per PRR
  Benefits:
    Smaller partial bitstreams
    Faster reconfiguration times
    Efficent area utilization in the FPGA
GOAL: High-level cost models for system designers
  Evaluation of design decisions early in the design process
    The cost models must provide sufficiently accurate evaluations
    Reduces design space exploration time
      As compared to full system implementation to attain same information
change to
PRR
PRR
PRR
PRR

## Slide 8: Contributions
Two high-level cost models for design decision evaluation
  Based on synthesis report results generated by Xilinx tools
  PRR size/organization cost model
    Compares PRRs with different resources and FPGA fabric locations
  Partial bitstream size cost model
    Partial bitstream size derivation based on PRR size/organization
Benefits of our cost models
  Early estimation of PRR size/organization and partial bitstream size
    Increases the resource utilization in PRRs
  Generally portable across different Xilinx FPGA families
    Device-specific characteristics’ values used in cost model formulas
  Does not require executing the entire PR design flow
  Significantly decreases the design exploration time
    Increasing system designer productivity

## Slide 9: PRR Size/Organization Cost Model

## Slide 10: PRR Size/Organization Cost Model Parameters
Specific values in PRR size/organization cost model for Virtex-4, -5, and -6 device families
Parameter | Virtex-4 | Virtex-5 | Virtex-6
CLBcol | 16 | 20 | 40
DSPcol | 4 | 8 | 16
BRAMcol | 4 | 4 | 8
LUT_CLB | 8 | 8 | 8
FF_CLB | 8 | 8 | 16
Parameter | Description
DSPcol | DSPs in a column (per row)
BRAMreq | BRAMs required in PRM
WBRAM | BRAM columns in PRR
HBRAM | BRAM rows in PRR
BRAMcol | BRAMs in a column (per row)
CLBavail | CLBs available in PRR
FFavail | FFs available in PRR
DSPavail | DSPs available in PRR
BRAMavail | BRAMs available in PRR
H | Number of rows in the PRR
W | Number of columns in the PRR
PRRsize | Size of PRR
Parameter | Description
LUT_FFreq | LUT FF pairs required in PRM
LUTreq | Slice LUTs required in PRM
LUT_CLB | LUTs per CLB
FF_CLB | FFs per CLB
CLBreq | CLBs required in PRM
FFreq | FFs required in PRM
WCLB | CLB columns in PRR
HCLB | CLB rows in PRR
CLBcol | CLBs in a column (per row)
DSPreq | DSPs required in PRM
WDSP | DSP columns in PRR
HDSP | DSP rows in PRR
Based on Xilinx synthesis report results

## Slide 11: Derivation of the PRR Size/Organization
PRR size/organization depends on the specific FPGA selected
PRR height (number of rows)
PRR Width (number of columns)
Total PRR size
  CLB columns (WCLB)
  DSP columns (WDSP)
  BRAM columns (WBRAM)
Derive PRRs resources
  Maximum resource util.
BRAMs
DSPs
Flip-Flops
Extract resources required for PRMs that map to same PRR
Selected Device : 5vlx110tff1136-1
Slice Logic Utilization:
# of Slice Registers: 1592 of 69120 2%
# of Slice LUTs: 1527 of 69120 2%
# used as Logic: 1527 of 69120 2%
Slice Logic Distribution:
# of LUT Flip Flop pairs used: 2619
# with an unused Flip Flop: 1027 of 2619 39%
# with an unused LUT: 1092 of 2619 41%
# of fully used LUT-FF pairs: 500 of 2619 19%
# of unique control sets: 45
IO Utilization:
# of IOs: 38
# of bonded IOBs: 38 of 640 5%
Specific Feature Utilization:
# of Block RAM/FIFO: 4 of 148 2%
# using Block RAM only: 4
# of BUFG/BUFGCTRLs: 3 of 32 9%
# of DSP48Es: 4 of 64 6%
Generate
synthesis
report for
each PRM
Select an FPGA
for the PR system
H = HCLB = HDSP = HBRAM
W = WCLB + WDSP + WBRAM
PRRSIZE = H x W

## Slide 12: Partial Bitstream Size Cost Model

## Slide 13: Partial Bitstream Structure
Partial bitstream structure is similar across device families
  Initial words (IW)
    Synchronization of bitstream with configuration port (e.g., ICAP)
  Configuration words per PRR row (NCWrow)
    Access to CLBs, DSPs, BRAMs, and CLB flip-flops initialization
  BRAM data words per PRR row (NDWBRAM)
    BRAM initialization
  Final words (FW)
    Releases the ICAP, allowing other PRRs to be configured

## Slide 14: Partial Bitstream Size Cost Model Parameters
Specific values in partial bitstream size cost model for Virtex-4, -5, and -6 device families
Parameter | Virtex-4 | Virtex-5 | Virtex-6
CFCLB | 22 | 36 | 36
CFDSP | 21 | 28 | 28
CFBRAM | 20 | 30 | 28
DFBRAM | 64 | 128 | 128
FRsize | 41 | 41 | 81
IW | 12 | 16 | 20
FW | 108 | 114 | 113
FAR_FDRI | 5 | 5 | 5
Bytesword | 4 | 4 | 4
Parameter | Description
IW | Number of initial words
FW | Number of final words
FAR_FDRI | FAR/FDRI initialization words per row
NCWrow | Configuration words in a PRR row
NDWBRAM | BRAM initialization words in a PRR row
NCFCLB | CLB configuration frames in a PRR row
NCFDSP | DSP configuration frames in a PRR row
NCFBRAM | BRAM configuration frames in a PRR row
CFCLB | Configuration frames per CLB column
CFDSP | Configuration frames per DSP column
CFBRAM | Configuration frames per BRAM col.
DFBRAM | Initialization frames per BRAM col.
FRsize | Frame size in words
Bytesword | Number of bytes per word
H | Number of rows in the PRR
Sbitstream | Size of partial bitstream in bytes

## Slide 15: Partial Bitstream Size Derivation
Partial bitstream size in bytes
Sbitstream = {IW + H x (NCWrow + NDWBRAM) + FW} x Byteswords
PRR rows
frame size
NCWrow = FAR_FDRI + (NCFCLB + NCFDSP+ NCFBRAM + 1) x FRsize
Configuration words per PRR row
CLB configuration frames per PRR row
NCFCLB = WCLB x CFCLB
DSP configuration frames per PRR row
NCFDSP = WDSP x CFDSP
BRAM configuration frames per PRR row
NCFBRAM = WBRAM x CFBRAM
BRAM initialization words per PRR row
NDWBRAM = FAR_FDRI + (WBRAM x DFBRAM + 1) x FRsize

## Slide 16: Experimental Results

## Slide 17: PRR Size/Organization Cost Model Evaluation
RUCLB = 92%, RUDSP = 84%, RUBRAM = 0%
H = 1, WCLB = 5, WDSP = 2, WBRAM = 0
PRM FIR (Virtex-6)
Resource
Utilization
RUCLB = 82%
RUDSP = 80%
RUBRAM = 0%
H = 5, WCLB = 2, WDSP = 1, WBRAM = 0
PRM FIR (Virtex-5)
Resource
Utilization
RUCLB = 92%
RUDSP = 25%
RUBRAM =75%
H = 1, WCLB = 11, WDSP = 1, WBRAM = 1
PRM MIPS (Virtex-6)
Synthesis report results using Xilinx ISE 12.4 tools
Resource utilizations (RUs) per resource type are maximum for the selected PRR size/organization
Resource
Utilization (RU)
RUCLB = 97%
RUDSP = 50%
RUBRAM =75%
H = 1, WCLB = 17, WDSP = 1, WBRAM = 2
PRM MIPS (Virtex-5)
Executing the entire flow vs. using our cost model
  Average RUCLB is 15% higher (due to tool optimizations)
  RUDSP and RUBRAM are the same
FPGA devices -- Virtex-5 LX110T and Virtex-6 LX75T
  Different sizes/architectures to evaluate different resource organizations
Experimental PRMs -- MIPS, FIR, and SDRAM
  PRM complexity and resource usage similar to prior works

## Slide 18: Partial Bitstream Sizes
 | Virtex-5 LX110T |  |  | Virtex-6 LX75T |  | 
Process | FIR | MIPS | SDRAM | FIR | MIPS | SDRAM
Synthesis | 4m 25s | 4m 15s | 3m 20s | 4m | 4m 50s | 4m 23s
Implementation | 5m 35s | 5m 15s | 2m 55s | 4m 15s | 5m 50s | 4m 30s
Place and Route execution times
Includes derivation of PRR size/organization and bitstream size
(cost model = 1m 30s on avg., which is 35% of synthesis time)
Execution times: minutes (m) and seconds (s)
PRM | Virtex-5 LX110T | Virtex-6 LX75T
FIR | 83,440 | 77,340
MIPS | 157,672 | 189,140
SDRAM | 18,416 | 24,204
Bitstream sizes (in bytes) based on PRR sizes/organizations per PRM
  Without executing the entire PR design flow
  Bitstream sizes are 9% larger on average vs. executing the entire flow

## Slide 19: Conclusions
Introduced two high-level cost models
  Early design estimation tradeoffs for PR system design space exploration
  PRR size/organization cost model
    Smallest PRRs that maximize shared PRM resource utilization
  Partial bitstream size cost model
    Bitstream size derivation based on PRR size/organization
  Cost models generally portable across FPGA device families
  Improved system designer productivity
    Use of cost models without executing the entire PR design flow
Future work
  Introduce cost models as part of the PR design flow
    Integration with Xilinx tools in the PRR floorplanning process

## Slide 20: Questions?